## Slide 1: Design, modeling and control of bipedal laminate robot
Taha Shafa
Advisor: Daniel Aukes

## Slide 2: Outline

## Slide 3: Problem Statement
Laminate robotics contain many advantages in the cost and ease of manufacturability, however they are difficult to model and control
Currently there are not used for high precision applications
I want to show that a laminate robot can be designed, modeled, and controlled in such a way that will eventually allow for high precision applications with laminate robotics

## Slide 4: Challenges
Keeping costs down means cheap motors
  Cheap motors have less desirable properties
  Their behavior is harder to model/predict/control
High torque motors are needed for controls applications
  High torque motors are heavier
    Difficult to support weight of heavy motors with laminate materials
Flexible materials are difficult to model
  Flexible materials are more prone to degradation
  Their models will be completely changed if there are any unwanted bends or tears

## Slide 5: Background
What are laminate robots?
Why do we want to develop them?
What are the advantages and disadvantages of control algorithms?
Why are there not more control engineers implementing their knowledge onto laminate robotics?
How is my project addressing these issues?

## Slide 6: Laminate Robots
Flexible, easily printed materials used for robotics
Convenient for producing large quantities at low cost
Flexible nature could prove advantageous for certain applications

## Slide 7: Objective
Develop bipedal laminate robot platform with 2DoF
Multiple design iterations developed a prototype capable of standing and movement

## Slide 8: Current Design
Motors:
  3 Dynamixel XL-320 Motors
Board:
  OpenCM9.04
Laminate Material:
  Cardboard
    1.04 mm thick

## Slide 9: Modeling
Pynamics Simulations
  Kane’s method
Hand Calculations
  Lagrange
Rigid Body Dynamics
  Hand Calculations
  Pynamics
Soft Body Dynamics
  Pynamics

## Slide 10: Model illustration

## Slide 11: Pynamics Model

## Slide 12: Controls Algorithms
LQR
  Desirable sensitivity properties
  Ideal for balancing
Optimal Control
  Ideal for path following
  Potentially useful for walking
Potentially need to switch between two different kinds of control systems between balancing and walking

## Slide 13: Future Work
Adapt design to fit new motors
Implement model into LQR based controller and full state feedback controller
Adjust the model to account for flexible links
  Measure the flexibility of links used in future design
Compare and contrast different control systems paired with different models to conclude the efficacy of model based control on laminate materials

## Slide 14: Conclusion/Future Work
Optimization
Different Control Techniques
Laminate materials
Practical implementation of ideas in my thesis